| No. | Description | Options |
| --- | --- | --- |
| 0 | Custom Program set. You can have two completely separate groups of settings, in memory, for different applications. | 0-A: set #1 1-b: set #2 |
| 1 | Focus Priority with Continuous Servo AF | 0: release priority 1: focus priority |
| 2 | Focus Priority with Single Servo AF | 0: focus priority 1: release priority |
| 3 | Bracketing order | 0: center, down, up 1: negative value to positive value |
| 4 | Autofocus activated when shutter release button lightly pressed | 0: Enabled 1: Disabled |
| 5 | AE-lock: Shutter speed/aperture shift | 0: Enabled 1: Disabled |
| 6 | Direction of Command Dial rotation | 0: Default 1: Reversed |
| 7 | Auto Exposure lock when shutter release is lightly pressed | 0: Disabled 1: Enabled |
| 8 | Film advance with closing the camera back | 0: Disabled 1: Enabled |
| 9 | Film advance speed in CH | 0: 8fps CH8: 8fps CH6: 6fps |
| 10 | Film advance speed in CL | 0: 3fps CL5: 5fps CL4: 4fps CL3: 3fps |
| 11 | Warning LED blinks during bulb exposure | 0: Disabled 1: Blinks |
| 12 | Film advance stop | 0: Disabled E35: stops after frame 35 E36: stops after frame 36 |
| 13 | Multiple exposure mode cancellation | 0: Canceled after 2nd exposure 1: Enabled until reset manually |

Cut out the two tables above and paste them on a piece of card front and back and voila. Laminate the card to protect it.

Bren.

| 14 | Diameter of 75% area in center-weighted metering | 0: 12mm C8: 8mm C12: 12mm C15: 15mm C20: 20mm |
| --- | --- | --- |
| 15 | Delay time for meter auto switch-off | 0: 16 seconds L4: 4 seconds L8: 8 seconds L16: 16 seconds L32: 32 seconds |
| 16 | Delay time for self-timer | 0: 10 seconds L2: 2 seconds L3, L4,...up to L60: 60 seconds |
| 17 | Bracketing in manual exposure mode. | 0: shifts shutter speed 11A: shifts speed + aperture 10A: shifts speed (same as default) 01A: shifts aperture 00A: shifts flash output |
| 18 | Focus screen compensation | 0: zero -2.0 to +2.0: variable in .5 EV steps |
| 19 | Extended time exposure range | 0: Disabled 1: Enabled |
| 20 | TTL flash sync speed (default) | 0: 1/250 sec 1/300, 1/250, 1/200, 1/160, 1/125, 1/100, 1/80, 1/60 |
| 21 | AE-L / AF-L button options | 0: Simultaneous AE / AF lock AEL: AE lock only AFL: AF lock only L-L: double-lock (same as default) |
| 22 | Aperture setting with lens aperture ring | 0: Disabled 1: Enabled (set by lens aperture ring) |
| 23 | < and > focus indicators | 0: Displayed 1: not Displayed |
| 22 | Bracketing, existing light or flash | 0: both existing and flash 01E: existing only 10E: flash only 11E: both (same as default) |